## Slide 1
Designing and Simulating a Directionally Stable Sailboat
Jesse Miller, M.Eng, MAE
Cornell University, 2016

## Slide 2
Directional Stability-Basic Idea
Remain on-course without constantly steering (no onboard power)
Desired course
Actual Trajectory
Actual Trajectory
Desired course
Unstable
Stable

## Slide 3
Designs to be Tested
Water Rudder
Air Rudder
Tail
=

## Slide 4
Procedure
Model Forces
Simulate in MATLAB

## Slide 5
Sailboat Dynamics Model

## Slide 6
Dynamic Model
COM coordinates
Euler angles
Rotation rates in body frame
State representation

## Slide 7
Dynamic Model
Sail, Keel, Rudder are airfoils
airfoil
airfoil
airfoil
=

## Slide 8
Dynamic Model
Forces on Sail, Keel, and Rudder
Approximate as NACA 0015 airfoil
Relative Wind

## Slide 9
Dynamic Model
Blade Element Theory
Rotational velocity of boat causes non-uniform flow over airfoils
Relative Wind
1
2
3
Example with 3 elements:

## Slide 10
Dynamic Model
Hull Buoyancy
Assume ellipsoid
=
  Hull (ellipsoid)
Submerged Volume

## Slide 11
Dynamic Model
Hull Buoyancy
Approximate submerged volume with sinusoid
  Draft

## Slide 12
Dynamic Model
Buoyancy Simulation

## Slide 13
Dynamic Model
Pitching Moment
Second moment of area of waterplane:
Acceleration due to gravity:
Water density:
Pitch angle:
Gained buoyancy
Lost buoyancy
d
Side View of Hull:

## Slide 14
Dynamic Model
Hull Resistance (Drag)
Wave-making resistance
Analyzed experimentally
Boat Hull
Pulley
Weight

## Slide 15
Free Body Diagrams

## Slide 16
Sailboat Simulation

## Slide 17
Sailboat Simulation
Linear Momentum Balance
Angular Momentum Balance
Kinematics
Numerically solve in MATLAB with ode45
COM coordinates
Euler angles
Rotation rates in body frame

## Slide 18
Sailboat Simulation
Animation

## Slide 19
Stability Test and Results

## Slide 20
Test Stability in Simulation
Air Rudder
Water Rudder
Tail

## Slide 21
Inherent Directional Stability:
Return to desired heading regardless of initial heading
Resist small disturbances (wind gust)
Sail with stability both upwind and downwind
Do all this without constant energy expense or mechanical response
Inherent Directional Stability

## Slide 22
Test Stability in Simulation
Water Rudder
Inefficient (very slow) stable sailing directions

## Slide 23
Test Stability in Simulation
Air Rudder
Limited range of stable directions:
True Wind
Small disturbance causes stable rudder force
disturbance
Small disturbance causes unstable rudder force
disturbance

## Slide 24
Test Stability in Simulation
Tail
True Wind
Moment turns boat
Boat stability in right direction

## Slide 25
Test Stability in Simulation
Independent of initial orientation in 3D simulation (for small lean)
Tail
It’s Stable!

## Slide 26
Test Stability in Simulation
2 stable equilibrium solutions in 3D simulation when lean angle becomes large.
Tail

## Slide 27
Test Stability in Simulation
Explanation for multiple stable sailing directions in 3D simulation

## Slide 28
Test Stability in Simulation
Explanation for multiple stable sailing directions in 3D simulation

## Slide 29
We’ve created a MATLAB sailboat simulation to verify direction stability
We’ve designed a directionally stable sailboat (using a tail design)
  Certain conditions create multiple stable directions. We will look into fixing this.
Cornell Autonomous Sailboat Team built the tail design this semester.
Testing at Cayuga lake this weekend!
Conclusions

## Slide 30
References
[1]
True Wind Speed |  |  | Ballast Mass |  | 
Sail | Chord Length |  | Water rudder | Chord Length | 
 | Span |  |  | Span | 0.
 | Mass |  |  | Mass | 
 | Distance in front of C.O.M. |  |  | Distance in front of C.O.M. | 
Keel | Chord Length |  | Air rudder/ Tail | Chord Length | 
 | Span |  |  | Span | 
 | Mass |  |  | Mass | 
 | Distance in front of C.O.M. |  |  | Distance in front of C.O.M. | 
True Wind Speed |  |  | Ballast Mass |  | 
Sail | Chord Length |  | Water rudder | Chord Length | 
 | Span |  |  | Span | 
 | Mass |  |  | Mass | 
 | Distance in front of C.O.M. |  |  | Distance in front of C.O.M. | 
Keel | Chord Length |  | Air rudder/ Tail | Chord Length | 
 | Span |  |  | Span | 
 | Mass |  |  | Mass | 
 | Distance in front of C.O.M. |  |  | Distance in front of C.O.M. | 

## Slide 31
Questions?